## Slide 1: FEM Simulation before Fabrication
Arjun Narayanan
Lucas Smyk

## Slide 2: Problem and Motivation
Problem
Simulate the behavior of elastic materials before fabrication
Motivation
Because 3D printing an object is costly in time and materials, we want our material to behave correctly prior to fabrication

## Slide 3: Derivation
Thanks to Desai Chen for resources on FEM theory
We took the derived all formulas ourselves

## Slide 4: Technical Approach – Hexahedral Elements
x = deformed space, X = reference space
Indirect formulation with potential energy function
Minimize the energy in the presence of external forces
Strain Energy Function

## Slide 5: Quadrature points
3D 2-point Gaussian Quadrature rule
8 quadrature points:

## Slide 6: Technical Approach continued
Express strain energy in terms of deformation gradient. Sum strain energy at each quadrature point.
Derivation for Fj
  Express shape function
  Take the derivative with respect to reference space coordinates

## Slide 7: Derivation for Fj
Shape function expressed with tri-linear interpolation
(uj expressed similarly)

## Slide 8: From F to : Material Model
Neohookean model:

## Slide 9: Energy Minimization
Gradient Descent
  Move in direction of force
Newton’s method
  Second derivative of V = stiffness matrix K
  Solve K * deltaX = f

## Slide 10: Newton’s Method
K is big – (3*numElements) x (3*numElements)
  Need sparse matrix representation!
Solvers:
  Eigen dense QR decomposition –TOO MUCH SPACE AND TOO SLOW
  Eigen sparse conjugate gradient – TOO SLOW
  CUSP GPU-Assisted sparse cg solver – WORKED WELL

## Slide 11: Makerbot Material Model
Didn’t have as much time to work on this
Measure Young’s Modulus of brick and convert to Neohookean parameters
Recreate cube experiment in simulation

## Slide 12: FEM Results
Demo Video
https://www.youtube.com/watch?v=6-0ZNnHaVS8

## Slide 13: Recreate cube experiment
Constructed material model: mu = 7.038*10^4, lambda = 1.056*10^5
Measured vs simulated data
(Simulation done with 1900 elements)
Error decreases with more force
FORCE (kg) | Measured Displacement of Cube (inches) | Simulated Displacement of Cube (inches) | Error (% of measured)
0.328 | 0.036 | 0.0236 | 34.4
0.72 | 0.061 | 0.0501 | 17.9
1.243 | 0.090 | 0.0800 | 11.1
1.78 | 0.099 | 0.105 | 6.06
Error decreases with more force

## Slide 14: Conclusions
FEM Simulation behaves accurately
Constructed material model does approximate actual behavior

## Slide 15: Future Work
Test more objects in reality vs simulation using constructed material model
  Ran out of time to do this
Measure stress at which material breaks

## Slide 16: Resources
As mentioned, thanks to Desai for some resources on Hexahedral elements
“Non-linear Continuum mechanics for finite element analysis” by Bonet and Woods
Class slides and notes for 6.S079
SIGRAPH 2012 course “FEM Simulation of 3D Deformable Solids: A practitioner's guide to theory, discretization and model reduction”