## Slide 1: FEM Simulation before Fabrication
Arjun Narayanan
Lucas Smyk

## Slide 2: Problem and Motivation
Problem
Simulate the behavior of elastic materials before fabrication
Motivation
Because 3D printing an object is costly in time and materials, we want our material to behave correctly prior to fabrication

## Slide 3: Derivation
Thanks to Desai Chen for resources on FEM theory
We took the resources and derived hexahedral FEM

## Slide 4: Technical Approach – Hexahedral Elements
x = deformed space, X = reference space
Indirect formulation with potential energy function
Force applied at vertices causes cube deformation to minimize potential energy

## Slide 5: Quadrature points
3D 2-point Gaussian Quadrature rule
8 quadrature points:

## Slide 6: Technical Approach continued
Express strain energy in terms of deformation gradient. Sum strain energy at each quadrature point.
Derivation for Fj
  Express shape function
  Take the derivative with respect to deformed space coordinates

## Slide 7: Derivation for Fj
Shape function expressed with tri-linear interpolation
(uj expressed similarly)

## Slide 8: From F to : Material Model
Neohookean model:

## Slide 9: Energy Minimization
Both gradient descent and Newton’s Method implemented
Can’t run Newton’s method yet because we need a sparse matrix solver
  Will use cusp

## Slide 10: Initial Results
Demo Video
https://www.youtube.com/watch?v=i7Q_NUDL1eU

## Slide 11: Test Material

## Slide 12: Issues and Remaining Work
Fix simulation collapse with multiple elements
Measure Makerbot material and integrate into code
Finish Newton’s method with cusp solver
Test simulation versus reality
Predict breakage

## Slide 13: Resources
As mentioned, thanks to Desai for some resources on Hexahedra's elements
“Non-linear Continuum mechanics for finite element analysis” by Bonet and Woods
Class slides and notes for 6.S079
SIGRAPH 2012 course “FEM Simulation of 3D Deformable Solids: A practitioner's guide to theory, discretization and model reduction”